Installation:
merX is made up of a single tar file that can be freely downloaded from merxedi.com. The following section will cover the installation instructions for Linux, since it is the recommended platform to use for these purposes. The server will also run on Windows and Mac as well but will require additional compiled versions of the merX binary for those platforms. Please contact us if you desire to run on those platforms or you can download the full source code and compile yourself.

If you wish to replicate the environment that merX was developed in, the following info should help: Ubuntu 14.04 LTS (linux), MariaDB 5.5, NGINX (pronounced “engine X”) v1.4.6 Web Server, and PHP v5.5.

Step One: Install Linux, preferably a Debian based flavor, onto a server with the necessary hardware to support your user base. In most cases this will not require a massive hardware platform to support and an average server should be more than sufficient.
Recommended:	install SSH (during Linux install)
set secure updates to Auto (during linux install)

After first boot up:	run apt-get update (requires sudo)
run apt-get upgrade (requires sudo)

Step Two: Load the MariaDB package onto the server. To do this go to https://downloads.mariadb.org/mariadb/repositories/ and follow the download instructions for your specific Linux OS and version. (merX was developed with MariaDB 5.5)

NOTE: You can also use MySQL as your database server if you like. There are no compatibility issues between the two but because of Oracle's stance on some of the MySQL changes ,as well as performance issues, we've standardized on the MariaDB branch.

Step Three: Install a web server, any flavor should work. MerX was developed using the nginx webserver with SSL enabled. It is strongly recommended that SSL be used.

If you wish to change the NGINX default web server port: navigate to the sites-available folder and change	the default file configuration. Typically it's /etc/nginx/sites-available/default and edit the port number from	the default of 80 to the port you wish to listen on. You will also find web urls to helpful NGINX resources in	this file. You can confirm NGINX version by entering: nginx -v at a command prompt.

Should see something like:	server {
listen 80 default_server;
listen [::]:80 default_server ipv6only=on;
…........
}

Note: Don't forget to restart the nginx service to put changes into effect. /etc/init.d/nginx restart [press Enter]

NGINX allows you to serve both HTTP and HTTPS requests simultaneously, and custom port choice. You will have to make sure you configure your SSL certificate correctly to avoid errors. Details of that are outside the scope of this document, but if you've purchased a SSL cert before then you already know how to do this.

If you wish to get involved in the source code of merX you can download the source code from merxedi.com. For most installations however, it's perfectly okay to just download the binary that is available on merxedi.com.

Download and untar the merx-xxx.tar.gz file using: “tar zxvf merx-xxx.tar.gz -C /usr/local/” (without the quotes). This will create /usr/local/merx/... and all of the necessary files will be located in that folder. The merx.conf file contains information necessary to start the server, such as the port you wish for it to attach to, and how it is to communicate with the database that you'll setup in step four. Please refer to the README file in the /usr/local/merx folder for more details on merX configuration options.

Step Four: Install php:
Example:	at the CLI, sudo apt-get install php5-cli (press Enter)
(confirm version by typing php --version [press Enter] at the command prompt)

Install PHP for processing:	sudo apt-get install php5-fpm php5-mysql [press Enter]
Configure the PHP processor:	sudo nano /etc/php5/fpm/php.ini [press Enter]
Note: search for cgi.fix_pathinfo=1, uncomment the line and change the 1 to 0, save and exit.
Restart the PHP processor:	sudo service php5-fpm restart [press Enter]

Step Five: Install the merX database by executing the script file located in the /usr/local/merx folder using: “mysql -u root -p < merx.sql” (without quotes).

Step Six: Configure your merx.conf file with the necessary information. See the notes in the README file for the necessary values.

Step Seven: Add the server to the startup scripts for the server. See the notes in the README file.

DaysToFullfill table requires something in it, or else getinventory will not work.